## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID - SIH26040
Problem Statement Title - Smart Water Purification and Quality Monitoring System for Rural and Mining-Affected Areas
Theme - Clean & Green Technology
PS Category - Hardware
Team ID - 158819
Team Name (Registered on portal) – Team_7

## Slide 2: IDEA TITLE Smart Water Purification & Quality Monitoring System
Proposed Solution (Describe your Idea/Solution/Prototype)
TEAM_7
Overview:
Real-time sensing: Continuously monitors key water-quality parameters.
Smart classification: Uses on-device ML to identify the type of contamination.
Adaptive purification: Routes water through only the treatment stages it needs, making it suitable for variable mining-affected water.
Problems with conventional water treatment units:
Fixed treatment pipeline regardless of contamination type
No real-time visibility into water safety for the community
Heavy-metal contamination from mining runoff often goes undetected
High maintenance downtime with no early-warning of filter fouling
Innovation and uniqueness of the solution:
On-device ML classifies contamination type, not just threshold breach
Adaptive treatment routing activates only the stages needed per batch
Electrochemical heavy-metal sensing (LMP91000 AFE) - rarely seen in low-cost systems
Post-treatment verification with automatic reject/divert safety interlock
Predictive filter-fouling alerts based on treatment efficiency trend
Prototype:
Sensor cluster + control board housed in a sealed IP65 enclosure
Multi-stage purification train: sediment -> carbon -> ion-exchange/electrocoagulation -> UV
Solar + LiFePO4 battery power unit for off-grid operation
LoRa-based telemetry to a village-level dashboard, with GSM/SMS fallback
Concept explanation
Adaptive routing: sensor readings are classified on-device (TensorFlow Lite Micro) to identify contamination type before selecting a treatment path.
Electrochemical AFE sensing: a three-electrode setup with the LMP91000 front-end detects heavy metals (Fe, Mn, As) without lab-grade equipment.
Closed-loop verification: treated water is re-tested before entering storage; a failed batch is automatically diverted back for re-treatment.

## Slide 3: TECHNICAL APPROACH
Hardware requirements:
ESP32-S3 microcontroller unit
pH, TDS, turbidity & ORP analog sensors
DS18B20 digital temperature probe
LMP91000 electrochemical AFE (heavy metals)
ADS1115 16-bit external ADC
Solenoid valves + MOSFET/relay drivers
LoRa SX1278 module, GSM/SMS fallback
Solar panel + LiFePO4 battery + charge controller
TEAM_7
Software requirements
Arduino / ESP-IDF firmware
TensorFlow Lite Micro (edge classification)
Proteus (circuit simulation)
Custom dashboard / mobile app (BLE-MQTT bridge)
GitHub Repo : https://github.com/Yuvaraaj-007/SiH-26040/tree/main
WORKFLOW
Sensing & power | Processing | Communication | Actuation
Regulated 12V/5V/3.3V power distribution | Adaptive treatment stage selection | Real-time alerts & notifications | Usage logging & auto-refill trigger
Signal conditioning & buffering | On-device ML contamination classification | Mobile app data ingestion | Clean water storage & tank-level monitoring
pH, TDS, turbidity & ORP sensors | Sensor calibration & filtering | Cloud dashboard sync | Batch verification & reject/divert logic
LMP91000 electrochemical AFE (heavy metals) | ADS1115 16-bit ADC acquisition | GSM/SMS fallback alerts | Multi-stage purification: sediment, carbon, UV
Multi-source water intake | ESP32-S3 microcontroller unit | LoRa SX1278 module | 12V pump/valve MOSFET driver

## Slide 4: FEASIBILITY AND VIABILITY
TEAM_7
ASPECT | FEASIBILITY | RISK/CHALLENGE | MITIGATION STRATEGY
Hardware and sensing | Low-cost analog sensors + LMP91000 AFE replace lab-grade heavy-metal testing equipment | Electrochemical sensor drift and fouling in silt-heavy mine runoff | Periodic auto-calibration cycle; pre-filter mesh to protect electrodes from silt
Computation and telemetry | ESP32-S3 runs TFLite Micro classification on-device; LoRa gives long range at low power | Limited connectivity in remote mining/rural zones; LoRa payload size constraints | GSM/SMS fallback for critical alerts; LoRa mesh relay between deployed units
Field and long-term viability | Solar + LiFePO4 removes grid dependency; multi-stage design adapts to seasonal contamination | Fluctuating solar input and battery degradation over multi-year field deployment | MPPT charge controller with margin sizing; predictive maintenance alerts for filter/battery health

## Slide 5: IMPACT AND BENEFITS
RURAL COMMUNITIES : Provides continuous access to verified safe drinking water without relying on periodic manual lab testing.
MINING-AFFECTED POPULATIONS : Targets heavy-metal and acidic-drainage contamination specific to mining zones, which standard filters typically miss.
PUBLIC HEALTH IMPACT : Reduces exposure to waterborne pathogens and heavy metals, lowering incidence of related illnesses in underserved areas.
ECONOMIC BENEFITS : Off-grid solar operation and adaptive treatment reduce running cost and consumable replacement compared to fixed-pipeline purification units.
ENVIRONMENTAL BENEFITS : Selective, on-demand treatment stage activation reduces unnecessary chemical/energy consumption versus always-on treatment trains.
TEAM_7

## Slide 6: RESEARCH AND REFERENCES
Water Quality Classification Using Machine Learning Algorithms – Elsevier https://www.sciencedirect.com/science/article/pii/S2214714422003646
Real Time Monitoring of Water Quality for Rural Areas – IEEE https://ieeexplore.ieee.org/document/10165824/
Resource Utilization of Acid Mine Drainage (AMD): A Review – MDPI https://www.mdpi.com/2073-4441/14/15/2385
Electrochemical Sensors for Heavy Metal Ion Detection in Aqueous Medium – ACS https://pubs.acs.org/acsodf/article/9/24/25493/410316/Electrochemical-Sensors-for-Heavy-Metal-Ion
Recent Trends in Electrochemical Methods for Real-Time Detection of Heavy Metals – Elsevier https://www.sciencedirect.com/science/article/pii/S2451910325001085
Membrane Fouling Prediction Using Machine Learning – Elsevier https://www.sciencedirect.com/science/article/pii/S0376738822005622
GitHub Repo : https://github.com/Yuvaraaj-007/SiH-26040/tree/main
TEAM_7